## Slide 1
VENUE & MACRO
ANTENNAS
META LENS
CLEANBEAM

## Slide 2: AAS metalens Technology
Dipole
Dielectric Lens
NO Lens
AAS Lens
90% AIR
8dBi Gain
18dBi Gain
18dBi Gain
Dipole
Dipole
Dipole
Dipole
Dipole
To be shared with close customers only
Not to be “emailed” or “left” with customers

## Slide 3: Single Beam Antennas
Sharp Roll-Off, Low-Sidelobes 17°x 17° & 35°x 35°

## Slide 4: Single Beam Antennas
Ultra sharp roll-off, Shaped “Square” beam 50° x 50°

## Slide 5: Cluster Beam Antennas
Fixed Tilt 4-beam

## Slide 6: Cluster Beam Antennas
RET-Adjustable 4-beam

## Slide 7: MultiBeam Antennas
4-beam RET

## Slide 8: MultiBeam Antennas
8-beam RET

## Slide 9: MULTI-BEAM ANTENNAS
12-BEAM RET
THIS SLIDE IS NOT COMPLETE

## Slide 10: V17-001-01-A0
2T2R Lens Antenna 17°x 17°
ELECTRICAL SPECIFICATIONS |  |  | 
Frequency Range (MHz) | 3300-4000 |  | 
 | 3300-3550 | 3550-3700 | 3700-4000
Polarization | ±45° |  | 
Gain (dBi) | 18.5 ± 0.2 | 18.4 ± 0.1 | 18.5 ± 0.4
Azimuth Beamwidth | 18.5° ± 1° | 17° ± 1° | 16° ± 0.5°
Elevation Beamwidth | 18.5° ± 1° | 17° ± 1° | 16° ± 0.5°
VSWR (Return Loss dB) | 1.5:1 (-14) |  | 
Front-to-Back Ratio, 180° ± 30° (dB) | > 30 | > 30 | > 30
Sidelobe (dB) | > 18 | > 18 | > 18
Isolation (dB) | > 25 |  | 
MECHANICAL SPECIFICATIONS |  |  | 
Length | 280 mm (11.0 in) |  | 
Width | 280 mm (11.0 in) |  | 
Depth | 276 mm (10.9 in) |  | 
Weight | 3.1 kg (6.9 lb) |  | 
Connector Type | (2x) 4.3-10 Female |  | 

## Slide 11: V35-001-01-A0
2T2R Lens Antenna 35°x 35°
ELECTRICAL SPECIFICATIONS |  |  | 
Frequency Range (MHz) | 3300-4000 |  | 
 | 3300-3550 | 3550-3700 | 3700-4000
Polarization | ±45° |  | 
Gain (dBi) | 11.9 ± 0.2 | 12 ± 0.2 | 12.5 ± 0.7
Azimuth Beamwidth | 41° ± 2° | 40° ± 2° | 36° ± 3°
Elevation Beamwidth | 41° ± 2° | 40° ± 2° | 36° ± 3°
VSWR (Return Loss dB) | 1.5:1 (-14) |  | 
Front-to-Back Ratio, 180° ± 30° (dB) | > 25 | > 25 | > 25
Sidelobe (dB) | > 16 | > 17 | > 18
Isolation (dB) | > 25 |  | 
MECHANICAL SPECIFICATIONS |  |  | 
Length | 120 mm (4.7 in) |  | 
Width | 120 mm (4.7 in) |  | 
Depth | 120 mm (4.7 in) |  | 
Weight | TBD |  | 
Connector Type | (2x) 4.3-10 Female |  | 

## Slide 12: V50-001-01-A0
Sharp Roll-Off 2T2R Lens Antenna - 50° x 50°
ELECTRICAL SPECIFICATIONS |  |  | 
Frequency Range (MHz) | 3300-4000 |  | 
 | 3300-3550 | 3550-3700 | 3700-4000
Polarization | ±45° |  | 
Gain (dBi) | 10.9 ± 0.5 | 11 ± 0.2 | 11.5 ± 0.6
Azimuth Beamwidth | 49° ± 2° | 50° ± 1° | 51° ± 1°
Elevation Beamwidth | 49° ± 2° | 50° ± 1° | 51° ± 1°
VSWR (Return Loss dB) | 1.5:1 (-14) |  | 
Front-to-Back Ratio, 180° ± 30° (dB) | > 25 | > 25 | > 25
Sidelobe (dB) | > 15 | > 16 | > 17
Isolation (dB) | > 25 |  | 
MECHANICAL SPECIFICATIONS |  |  | 
Length | 260 mm (10.3) |  | 
Width | 260 mm (10.3) |  | 
Depth | 150 mm (5.9) |  | 
Weight | TBD |  | 
Connector Type | (2x) 4.3-10 Female |  | 

## Slide 13: AAS 4-beam Macro
concept

## Slide 14: AAS 4-beam Macro
concept
17 HBW
8.5 VBW
0 - 12 EDT

## Slide 15: AAS 4-beam Macro
CONCEPT

## Slide 16: AAS 4-beam Macro
Advantages
Better capacity solution than 64T64R with 8T8R radio configured into split sector mode
  Purely symmetric 4 beams with very low sidelobes
  No gain loss due to array scanning
  No grating lobes due to array scanning
Adjustable beam pairs
Ultra low loss / high gain beams
  No lossy RF PCB matrix to generate multiple beams
  Simple, low-loss phase shifter to generate tilt

## Slide 17: CLEANbEAM ROADMAP 2024-2025
C-Band
Mid-Band
Sept 2024
Oct 2024
Dec 2024
Q1 2025
Q2 2025
V17-001-01-A0
17x17
Single Beam
V35-001-01-A0
35x35
Single Beam
V50-001-01-A0
50x50
Square Beam
V35-001-01-A0
35x35 Single Beam
V35-001-04-A0
35x35
Cluster Beam
V17-010-01-A0
17x17 Single Beam
V50-010-01-A0
50x50 Square Beam
V35-001-04-A1
35x35 RET
Cluster Beam
V35-010-04-A0
35x35 Cluster Beam
V17-011-01-A0
17x17 Single Beam
V50-011-01-A0
50x50 Square Beam
V35-011-01-A0
35x35 Single Beam
V35-011-04-A0
35x35 Cluster Beam
M4-004A-LA0
Multi-Beam
M8-008A-LA0
Multi-Beam
MX-048A-LA0
Multi-Beam